## Slide 1
📱 Phone Test Builder
Web UI User Manual
ADB-based Phone Automation System
Version 1.0 · Mobicom

## Slide 2
Overview
🖱️ Drag & Drop
Build test workflows visually — no code needed
👁️ Live Preview
See steps as a formatted table in real time
⚙️ Device Config
Edit phone numbers & serials directly in browser
▶ Run Tests
Stream live PASS/FAIL results from the browser
📊 Reports
Pass rate bar, stat cards, full results table
📁 Templates
Save and reload named workflows (localStorage)
⬇ Export Excel
Generate xlsx compatible with the CLI runner
🏠 Auto Home
Devices return to home screen after test ends

## Slide 3
Getting Started
1
Enable USB Debugging
Settings → Developer Options → USB Debugging ON on each phone
2
Connect via USB
Plug both phones into the PC. Run: adb devices — both serials must appear
3
Edit config.py
Set DEVICES serial numbers and PHONE_NUMBERS for each phone
4
Install requirements
pip install flask openpyxl
5
Launch
Double-click start_web.bat OR run: python web_builder.py
6
Open browser
Navigate to http://localhost:5000

## Slide 4
Interface Layout
Header Bar — Title | + Section | Clear | 📁 Templates | ⬇ Export | ▶ Run Test
Left Sidebar Actions Palette (drag to canvas) ──────── Devices Panel Phone1 / Phone2 Serial + Number 💾 Save config
Editor Pane Drag & drop steps here Edit fields inline Reorder by dragging
Preview Pane # Action Target 1 📞CALL Ph1 2 📲ANSW Ph2 3 ⏳WAIT Ph1 ────────── 4 💬SMS Ph1
← Sidebar
← Editor Pane →
Preview →

## Slide 5
Actions Reference
📞 CALL
Dial a phone number from the target device.
📲 ANSWER_CALL
Wait for incoming ring then answer automatically.
📵 END_CALL
Hang up the active call.
⏳ WAIT
Pause execution for N seconds between steps.
💬 SMS
Send a text message from the target device.
🔍 CHECK_SMS
Verify an SMS was received from a given sender.
📋 CHECK_CALL
Verify a call entry exists in the call log.
📶 CHECK_VOLTE
Verify VoLTE is active via IMS registration and network type.
📡 USSD
Dial a USSD code and capture the network response.
📶 SET_NETWORK
Change the preferred network mode.
💡 WAKE
Wake and unlock the device screen.
⚙️ SET_CONFIG
Set an Android settings key via ADB.
🔧 GET_CONFIG
Read an Android settings key via ADB.

## Slide 6
Building a Workflow
1️⃣
Add Steps
Drag actions from the palette OR double-click them
2️⃣
Add Sections
Click "+ Section" → type the section title → press Enter
3️⃣
Fill Fields
Set Target Phone, Number/Code, Value, Expected Result
4️⃣
Reorder
Drag the step header OR use ▲▼ buttons in toolbar
5️⃣
Duplicate
Click ⎘ on any step to copy it
6️⃣
Delete
Click ✕ on a step, or select + Delete button in toolbar
7️⃣
Save Template
📁 Templates → enter a name → 💾 Save current
8️⃣
Export
⬇ Export Excel → downloads test_cases.xlsx

## Slide 7
Running Tests
How to run:
1
Click ▶ Run Test in the header bar
2
The run panel opens, covering the canvas
3
Each step shows blue 'running…' badge while executing
4
Results update live: ✓ PASS | ✗ FAIL | — SKIP
5
Live counter tracks totals in the panel header
6
Click ■ Stop at any time to abort
7
Devices return to Home Screen automatically when done
8
Click 📊 View Report to see the full summary
Result badges:
PASS
Action succeeded (and Expected Result matched if set)
FAIL
Action failed or Expected Result not found in output
SKIP
Action not supported or dry-run mode
running…
Step is currently executing

## Slide 8
Reports & Templates
📊 Test Report
11 Total
9 Passed
2 Failed
0 Skipped
82%
# Action Target Result Output
1 📞 CALL Phone1 PASS Starting: Intent...
2 📲 ANSW Phone2 PASS Call answered
3 📶 VOLTE Phone1 PASS VoLTE ACTIVE — IMS
4 💬 SMS Phone1 FAIL Send button not found
📁 Template Manager
⭐ Default Template built-in [Load]
Regression Test 8 steps · 6/10 [Load][✕]
VoLTE Test 4 steps · 6/10 [Load][✕]
Template name…
💾 Save
• Stored in browser localStorage — survives page refresh
• Overwrite: save with the same name
• Works across test sessions on the same machine

## Slide 9
Device Configuration
Devices
🟢 Phone1
connected
Serial
RF8Y606FYXX
Phone Number
+97694310546
🟢 Phone2
connected
Serial
4B270DLAQ003DE
Phone Number
+97695091051
💾 Save to config.py
Find your serial
Run: adb devices in a terminal with phone connected
Online indicator
🟢 Green = ADB connected ⚫ Grey = not detected
Refresh status
Click "↻ refresh" to re-check ADB connection in real time
Save changes
"💾 Save to config.py" writes both serial and phone number

## Slide 10
Tips & Troubleshooting
💡 Best Practices
• Run CHECK_VOLTE during an active call (after CALL + ANSWER_CALL) for accurate results • Add WAIT (5–10s) after SMS before CHECK_SMS to let the message arrive • Use sections to group related steps — they appear as dividers in the report • Name and save your workflow as a template before running
🔴 Common Issues
• Device offline: check USB cable, re-enable USB debugging, run adb devices • ANSWER_CALL timeout: increase Value to 30s if the ring takes longer • CHECK_SMS fails: add a longer WAIT before it, or check sender number format • USSD no response: the carrier may block ADB-initiated USSD on some SIMs
✅ VoLTE Testing
• Workflow: CALL → ANSWER_CALL → CHECK_VOLTE (both phones) → END_CALL • imsCallType=2 in telephony.registry = VoLTE confirmed • If result is 'no active call': run CHECK_VOLTE while call is still connected • Ensure 4G/LTE network and 'Enhanced 4G LTE' is ON in mobile settings
⚙️ Configuration
• Edit config.py OR use the Devices panel in the web UI — both update the same file • ADB_PATH in config.py must point to your adb.exe on Windows • Restart start_web.bat after changing config.py outside the web UI • Templates are browser-local (localStorage) — not shared between machines

## Slide 11
📱 Phone Test Builder
Start the web UI: python web_builder.py or start_web.bat
Open browser → http://localhost:5000
Mobicom · Phone Automation System · Version 1.0